## Slide 1: TDT4258: Low-Level Programming
Caches
Virtual Memory
Rakesh Kumar
Computer Architecture Lab
Department of Computer Science
Some of the slides are based on other courses around the world: University of Edinburgh, NTNU, etc.

## Slide 2
Cache organizations
Direct mapped
  A block can be placed only by one location in the cache
Fully associative
  A block can be placed anywhere in the cache
n-way set associative
  A block can be placed at one of the predetermined n locations in the cache

## Slide 3
Cache hit/miss
Problem with Direct Mapped Caches
1-byte
0000
0001
0010
0011
1111
16-entries
Memory
Address
0100
0101
0000
0101
0111
…
1000
Tag
0
Valid
1-byte
1-byte
Data
Cache
0
0
1
0100
0000
0100
0000
0100
1
Miss
00
Miss
01
Miss
00
Miss
Miss
Miss
An access evicts the data brought in by the previous access
All accesses compete for the same cache location
All other locations are empty

## Slide 4
Fully Associative Caches
1-byte
0000
0001
0010
0011
1111
16-entries
Memory
Address
0100
0101
0000
0101
0111
…
1000
Tag
Valid
1-byte
1-byte
Data
0
0100
0000
0100
1
Miss
00
Miss
01
Hit
Hit
0
1
0010
Hit?
Q: What do we use it for?
A: Use it as part of the tag.
Index bits in Direct Mapped cache become part of tag in Fully Associative cache.
000
010

## Slide 5
Fully-associative caches
tag
data block
valid
tag
byte offset
requested address:
Cache
Correct cache block identified by matching tags
Address tag can potentially match tag of any cache block
Byte offset selects word/byte within block

## Slide 6
Set Associative Caches
Problems with other cache organizations:
  In a direct-mapped cache, several addresses might compete for a few cache location while the other locations remain unused, thus lowering cache hit rate.
  In a fully-associative cache, search for matching tags is either very slow, or requires a very expensive memory type called Content Addressable Memory (CAM)
Set associative cache offer a compromise between direct mapped and fully associative caches.

## Slide 7
Set Associative Caches
Address
00000
Tag
Valid
1-byte
1-byte
Data
Direct Mapped Cache
Address
00000
Tag
Valid
1-byte
1-byte
Data
00
01
10
11
Index bits pick one cache block for tag comparison.
Index bits pick n cache blocks (one set) for tag comparison, where n is called the number of ways in the cache.
0
1
Set
Set
Set
2-way Set Associative Cache

## Slide 8
Set Associative Caches
00000
Tag
Valid
1-byte
1-byte
Data
Direct Mapped Cache
00000
Tag
Valid
1-byte
1-byte
Data
00
01
10
11
0
1
Set
Set
Set
Address
00000
Tag
Valid
1-byte
1-byte
Data
0
1
Set
Set
Address
Address
2-way Set Associative Cache
Set
Fully Associative Cache

## Slide 9
Block (or line): the unit of data stored in the cache
  Typically in the ranges of 32-128 bytes
Set: A group of blocks
Way: A block in a set
  Number of ways defines number of blocks in a set
  E.g. a 4-way set associative cache has 4 blocks in each set
  2 to 32 ways are common
  Fully associative cache: #ways = #blocks
Caveat: “Index” bits in address do not select a cache block, rather a cache set.
More cache terminology

## Slide 10
Cache replacement
What to do when we run out of cache space
  Need to evict a block to make space for the new one
Which block to evict?
  The block which is not going to be used soon
Replacement policies
  Random
  LRU (Least Recently Used)
  FIFO (First In First Out)
  ….

## Slide 11
Cache replacement
Least Recently Used (LRU)
  Evict the cache block that hasn’t been accessed longest
  Relies on past behaviour as a predictor of the future
  Complex implementation
FIFO – replace in same order as filled
  Simpler to implement
Example:
  address references: 0 2 6 0 7 8
  Cache with 4 blocks
0
2
6
7
8
0
0
2
6
7
0
LRU
FIFO
8

## Slide 12
Writing to caches
When to write the modified data to memory?
  Write-back: When the block is evicted
  Write-through: While writing to cache
Write-back:
  Pro: Consolidate multiple writes to the same block
    Saves bandwidth and energy
  Con: Need to track dirty (modified) blocks
Write-through:
  Pro: Simpler implementation and coherence.
  Con: Slow, bandwidth intensive

## Slide 13
Write-through
Always write to memory
Write is as slow as write to memory (not cache)
13
Data
Data
0
0
0
0
0
V
Tag
0x00 000000 32
0x04 000100 20
0x08 001000 16
0x0c 001100 00
0x10 010000 03
0x14 010100 00
…
CPU
store 24  0x8
100
16
00
1
24
24

## Slide 14
Write-back
Write only to cache
Write happens at the speed of cache
Data
Data
0
0
0
0
0
V
Tag
0x00 000000 32
0x04 000100 20
0x08 001000 16
0x0c 001100 00
0x10 010000 03
…
CPU
store 24  0x8
100
16
00
1
24
0
0
0
0
1
D
Note: the cache and memory are now not the same!
When we evict a line we need to know if it is different from the DRAM to write it back
Dirty bit keeps track of whether the cache block has been written.
If it is dirty, we need to write it back to DRAM when we evict it.

## Slide 15
Cache performance
AMAT = (hit rate * hit-time) + (miss rate * miss-latency)
Hit time = 1
Miss latency = 4
Hit
Miss
Miss rate = 2/6 = 33%; hit rate = 4/6 = 66%
AMAT = (0.66)*1 + (0.33)*(4) = 2.0 cycles per access
Hit
Miss
Hit
Miss
Hit
Mem
Mem
Mem
Mem
Mem
Mem
Hit

## Slide 16
Cache hierarchy
Multiple level caches to balance capacity and access latency
Typically caches at all levels are made of SRAM
Cache closest to processor is small but fast
Caches further away from processor are increasingly bigger but slower
  As size of SRAM grows, its access latency also increases
CPU
L1 cache
L2 cache
Last level cache
(LLC)
1-4 cycles
~10 cycles
30-60 cycles

## Slide 17
Virtual memory

## Slide 18
Motivation
Virtual memory addresses two main issues
Capacity: how to relieve programmers from dealing with limited main memory capacity?
  To allow physical memory to be smaller than the program’s address space (e.g. 32bit  4GB)
  To allow multiple programs to share limited physical memory
Safety: how to enable safe and efficient sharing of memory among multiple programs
  To prevent user programs to access memory used by OS
  To control the access by one user program to the memory of other user programs

## Slide 19
Virtual memory
Idea: make each program think that it owns the entire memory.
Virtual address space: addresses visible to the programmer
  E.g. PC, load/store addresses
Physical address space: actual main memory addresses
  Addresses used to access cache/ memory
Address translation
  Virtual address are translated on-the-fly to physical addresses
  The translation is done jointly by hardware and OS
  Parts of virtual address space not used recently is store on disk, not in memory

## Slide 20
Address Translation
Two styles of address translation
  Paging: Basic translation units are fixed size memory regions, called pages.
  Segmentation: Basic translation units are variable size memory regions, called segments.
We will focus on paging as it is used more commonly

## Slide 21
Paging
A cache line or block of virtual memory is called a page
  “page” or “virtual page” for virtual memory
  “page frame” or “physical page” for physical memory
Typical page sizes are 4-8 KB (MB or GB in servers)
  Large enough for efficient disk use and to keep translation tables (aka page tables) small
Translation is done through per program page tables
  Different programs can use same virtual address

## Slide 22
Virtual to physical mapping for 1 program
Virtual Address Space (4 GB)
0
232-1
212
Physical Memory (1 GB)
A
B
C
D
A
C
B
D
Disk
0
Hardware/OS
230-1
OS Virtual Memory Manager
Cache for disk

## Slide 23
Page address translation
Page offsets not translated
Page number is translated via page table
Example: 1KB pages
virtual address: 32 bits V O
page number
(22 bits  4M pages)
page offset (10 bits  1KB)
F O
physical address: 30 bits (1GB of main memory)
+
page table base address (physical)
Page table entry (PTE)
frame number |  |  |  |  |  | 
 |  |  |  |  |  | F
status bits |  |  |  |  |  | 
Page table is stored in main memory

## Slide 24
What is the size of the page table given a 32-bit virtual address space, 4 KB physical pages, and 1 GB of main memory?
Page offset: 12-bits
Virtual page number: 32-12 = 20-bits  1M page table entries
Status bits: 6-bits
Physical page number: 30-12 = 18-bits
Page table entry size: 18+6 = 24-bits
Page table size: 24Mbits = 3MB
Practice problem
Do all applications use all of these entries?

## Slide 25
Page table size:
  3MB
Each application requires its own page table
  100 concurrently executing applications would require 300MB for page tables
  1/3 of physical memory (300MB of 1GB) is used up for page tables only
Waste of space if an application uses only a fraction of its virtual address space
  One level page table reserves space for all possible virtual pages
Problem with one level page tables

## Slide 26
The last level tables hold the physical page number
A table at any other level holds pointer to tables at the next level.
Advantage: tables are inserted only if the corresponding part of the address space is in use
Multi-level page tables
Physical
page

## Slide 27
Storage cost for two level page table
virtual address: 32 bits V O
10 bit
10 bit
12 bit
1024-entries
1024-entries
1024-entries
Storage per table:
  3KB (1K entries, 3B/entry)
Covering full address space
  1025 table (1 at 1st level, 1024 at 2nd level)
  Storage: 3.003MB (1025*3KB)
    Slightly higher than single level page table
Covering smaller address space
  0x00000000 to 0x003FFFFF (4MB)
    Needs only 2 tables (1 at each level)
    Storage: 6KB
  0x00000000 to 0x7FFFFFFF (2GB)
    Needs 513 tables (512 at 2nd level)
    Storage: 513*3KB = 1.503MB
Page table storage varies with virtual address space actually used.

## Slide 28
Address translation with 2-level page table
virtual address: 32 bits V O
F O
physical address: 30 bits (1GB of main memory)
+
page table base address (physical)
10 bit
10 bit
12 bit
+

## Slide 29
Fast page table access
Problem: page table access adds to memory access latency
  Two memory accesses per load/store (for single level page table)
    one to get page table entry, one for actual load/store
  Page table is in main memory, though data may be in cache
Solution: Translation Lookaside Buffer (TLB)
  TLB is cache (typically fully associative) for page table
  Small fast table located close to processor
  Captures most translations due to principle of locality
  TLB miss: translation not in TLB. Access page table and save the translation in TLB

## Slide 30
TLB
TLB status bits
V (valid) bit
D (dirty) bit indicates whether page has been modified
R, W, X permission bits. Checked on every memory access
Virtual Page Number
PageOffset
31 12 11 0
Virtual
Address
Physical Page Number (PPN)
Tag
V D R W X
=
=
=
=
=
TLB hit
Physical Page Number
PageOffset
31 12 11 0
Physical Address

## Slide 31
Integrating TLB with cache

## Slide 32
Virtual memory: full picture

## Slide 33
Want to learn more
  Computer Organization and Design, Patterson & Hennessy
Advanced courses
TDT4255-Computer Design and TDT4260-Computer Architecture
For projects and thesis opportunities, check out
Computer Architecture Laboratory
https://www.ntnu.edu/idi/lab/cal
Advertisement