## Slide 1: TDT4258: Low-Level Programming
- Introduction to ARM Assembly Language
Rakesh Kumar
Computer Architecture Lab
Department of Computer Science
Some of the slides are based on other courses around the world: ETHZ, University of Edinburgh, NTNU, etc.

## Slide 2
What is an Embedded System?
Text book definition
Any device that includes a programable computer but is not itself a
general purpose computer.
An alternate definition
A computing system, specialized for only few applications with
none (or minimum) end user programmability, embedded into a
larger product.
- The main purpose of the product is not computing.

## Slide 3
Embedded System examples
You don’t buy any of these for computing!

## Slide 4
What’s in the name!
© Edward Lee

## Slide 5
Embedded System market
100,000
10,000
1,000
100
10
1
Servers
Personal Computers
Mobile Devices
Embedded
Units shipped per year (millions)

## Slide 6
Do Embedded Systems have future?
Manyika, James, et al. Disruptive technologies: Advances that will transform life, business, and the global economy. Vol. 180.
Embedded Systems are an essential component
…
San Francisco, CA: McKinsey Global Institute, 2013.

## Slide 7
Let’s dig in!

## Slide 8
Embedded Systems: A pictorial view
physical/biological/social processes
CYBER WORLD
PHYSICAL WORLD
Nature
Hardware &
Software
Computation
reasoning deciding big data
Communication
observing influencing
Embedded System
Use feedback to influence the dynamics of the physical world by taking smart decisions in the cyber world

## Slide 9
Predictability
Dependability
Efficiency
  Energy and run-time efficient
  Weight and cost efficient
Embedded Systems: Design objectives
“It is essential to predict how a CPS (cyber‐physical system) is going to behave under any circumstances […] before it is deployed.”Maj14
“CPS must operate dependably, safely, securely, efficiently and in real‐time.”Raj10
Maj14 R. Majumdar & B. Brandenburg (2014). Foundations of Cyber‐Physical Systems.
Raj10 R. Rajkumar et al. (2010). Cyber‐Physical Systems: The Next Computing Revolution.

## Slide 10
Reactive: Must react to stimuli from environment
Time constrained: must meet real-time constraints
  For hard real-time systems, right answers arriving too late are wrong.
Specialized: specialized towards few applications or domains
  Domain knowledge helps optimize the design e.g. minimize resource usage, maximize predictability, etc.
“A real‐time constraint is called hard, if not meeting that constraint could result in a catastrophe” [Kopetz, 1997].
Embedded Systems: Properties
“A reactive system is one which is in continual interaction with is environment and executes at a pace determined by that environment” [Bergé, 1995]

## Slide 11
Few applications (known at design time)
Not programmable by end user.
Fixed performance requirements (additional performance not useful)
Design criteria
  Cost
  Power consumption
  Worst case speed
  Size and weight
  Dependability
Embedded vs General Purpose Systems
Broad range of applications
Programmable by end user.
Higher performance is useful (enables new applications)
Design criteria
  Cost
  Power consumption
  Average speed
Embedded Systems
General Purpose Systems

## Slide 12
Embedded System design flow
Requirements
Specification
Architecture
Components
Integration
Top-down design
Bottom-up design

## Slide 13
Requirements
Informal description of the system in layman’s language.
Functional: Answers the question-“What should the system do?”
  E.g.: A GPS Moving Map should display the map of terrain around user’s current position.
Non-functional: Requirements not related to the functionality such as cost, size, power, etc.
  E.g.: GPS Moving Map should cost under NOK 1000, fit on the palm, and run for atleast 8 hours on two batteries.
Designing Embedded Systems
Specification
Architecture
Components
Integration

## Slide 14
Specification
An unambiguous technical description derived from Requirements. Detailed enough to design the system architecture.
Examples:
  Fit on palm: 2” x 4”
  8 hours on batteries: 100mW
Designing Embedded Systems
Requirements
Architecture
Components
Integration

## Slide 15
Architecture
A high level overview of system structure in term of components needed and their interaction.
Key Challenge: How to distribute the functionality among hardware and software to meet the competing requirements: cost, performance, power..
Designing Embedded Systems
Requirements
Specification
Components
Integration

## Slide 16
Components
Choose or build the component to implement the Architecture and meet the Specifications.
Standard components: CPUs, memory, software libraries, …
  GPS receiver and topographic database are standard components
Custom components: Printed circuit boards, software modules, …
  User interface is a component that might need custom design
Designing Embedded Systems
Requirements
Architecture
Specification
Integration

## Slide 17
Integration
Put the components together and make the system work!
Key Challenge: Unforeseen bugs popup during integration.
Requires debugging
Careful component designing can help a lot.
Designing Embedded Systems
Requirements
Architecture
Specification
Components

## Slide 18
Embedded System: Hardware (H/W)
CPU
Memory
I/O devices
BUS

## Slide 19
Embedded System: Programming the H/W
CPU
Memory
I/O devices
BUS
C - Code
Assembly Code
Operating System
Compiler, Assembler, Optimizer
H/W

## Slide 20
Let’s do something fun!

## Slide 21
Why learn it?
  Fun to talk to a processor in its native language
  Most efficient way to program a processor (if you can get the code right!)
We will examine ARM ISA to learn assembly
  ARM: Most popular mobile and embedded ISA.
  ISA: Instruction Set Architecture
Assembly Programming

## Slide 22
Programmer’s view of hardware
Interface between hardware and software
  Defines processor recognizable machine instructions
  Defines architecture state, memory management,…
Why is it useful?
  Abstracts away hardware implementation details
  Software can be developed (somewhat) independent of hardware implementation
  Enables multiple implementations (called Microarchitectures) of the same ISA
Instruction Set Architecture (ISA)

## Slide 23
Machine instructions
  Strings of binary numbers
  Example: 01001011010100101011010010001010
  Processor works with machine instructions but they are difficult for humans to understand
Assembly instructions
  Symbolic representation of machine instructions
  Easier for humans to understand
  Strict one-to-one mapping between machine and assembly instructions
Machine and assembly instructions

## Slide 24
High level language (c/Java) code: a[0]=b[0]+5;
Assembly code:
  ldr r3,[r1] ; get the value to b[0] from memory to r3
  add r4,r3,5 ; add 5 to b[0] and store in r4
  str r4,[r2] ; save r4 to a[0]
Assembly code example
mnemonic: what operation to perform
Where is the data required to perform the operation
Where to store the result of the operation
Comments. For code readability. Start with ;

## Slide 25
Hight level language (c/Java) code: a[0]=b[0]+5;
Assembly code:
  ldr r3,[r1] ; get the value to b[0] from memory to r3
  add r4,r3,5 ; add 5 to b[0] and store in r4
  str r4,[r2] ; save r4 to a[0]
  Things to notice:
    Data needs to be brought to registers from memory to operate on it
    Separate instructions to access data (from memory) and operate on it
      Called load-store architecture
      An alternative architecture: register memory architecture
Assembly code example

## Slide 26
  ldr r3,[r1] ; get the value to b[0] from memory to r3
  add r4,r3,5 ; add 5 to b[0] and store in r4
  str r4,[r2] ; save r4 to a[0]
How many and what instructions are available?
  How long is an instruction?
Is there a limit on number of registers?
Does the address need to be in a register to access a memory location?
Food for thought!
All of these are architecture (ISA) specific.

## Slide 27
ARM is a load-store architecture
Offers several variants
  ARMv8: 64-bit architecture
  ARMv7: 32-bit architecture
    All instructions are also 32-bit
  Thumb architecture
    16-bit instructions to reduce code size
  Thumb-2 architecture
    Supports both 16-bit and 32-bit instructions
You will use Thumb-2 in the labs.
ARM architecture (ISA)

## Slide 28
Registers are storage locations inside the processor that hold program variables and control state
Thumb-2 provides 16 general-purpose registers (r0-r15) and a current program status register (CPSR). Each register is 32-bit wide
Registers
r0
r1
r2
r3
r4
r5
r6
r7
r8
r9
r10
r11
r12
r13 (SP)
r14 (LR)
r15 (PC)
0
0
31
31
CPSR
0
31
Negative | Zero | Carry | Overflow
SP: Stack Pointer
LR: Link Register
PC: Program Counter
31
28

## Slide 29
Memory access instructions
  To transfer data between registers and memory
  Only instructions that can access memory
  Examples: ldr, str, etc.
Arithmetic/logic instructions
  Perform the desired operation like: add, subtract, shift, or, and
  Operate only on registers
Control transfer (a.k.a. branch) instructions
  Control the flow of program execution
  Jumps, loops, etc.
More details in the text book and Thumb-2 manuals!
Thumb-2 Instruction Categories

## Slide 30
ARM Instruction Format
Not available for most of the Thumb2 instructions

## Slide 31
Preparing to write an assembly program
r2
232 - 4
0
4
8
32 bits
A[0]
A[1]
A[…]
Memory
Getting data from memory
High level language statement:
g = A[1] + 5
where
A[0] is the first element of array A and is pointed to by r2
Assembly code:
ldr r3, [r2, #4]
add r4, r3, 5
offset in bytes
Memory is byte addressable

## Slide 32
Writing an assembly program
High Level Language Code
Assembly Code
int a[2] = {10, 20};
int x;
x = a[0] + a[1];
.section .text
ldr r1, =a
ldr r2, [r1]
ldr r3, [r1, #4]
add r4, r2, r3
ldr r1, =x
str r4, [r1]
.section .data
a:
.word 10 ; a[0]
.word 20 ; a[1]
x:
.word 0 ; x
ldr is a pseudo-op here.

## Slide 33
Memory addressing: Endianness
Given a memory address, Endianness tells where to find the first byte of a word.
ARM supports both little and big endianness