## Slide 1: TDT4258: Low-Level Programming
Compilation and Optimizations
Rakesh Kumar
Computer Architecture Lab
Department of Computer Science
Some of the slides are based on other courses around the world: MIT, Georgia Tech, NTNU, etc.

## Slide 2: Previous Lecture
Intro to C (Pointers)
  Structures
  Arrays
  Strings
  Writing generic functions using pointers
  Memory management in C

## Slide 3: Today’s Lecture
Introduction to compilation and the compiler tool chain
  Introduction
  Compiler tool flow
  Compiler stages
    Preprocessing
    Frontend: Lexical (scanning) and syntactic analysis (parsing), semantic analysis
    Intermediate representations
    Backend: code generation and optimization
  Compiler optimizations in detail
  Assemblers, linkers and loaders

## Slide 4: Overview
Programs are divided into compilation units
  Provide degree of modularity
  Each commonly has main file (.c) for source code
  Header files (.h) declare public interfaces of units
Each unit is compiled separately to relocatable object code
  Allows creation of object-code libraries
A linker combines these into an executable, resolving references between units
A loader sets up the executable program in memory and initialises data areas, prior to the program being run

## Slide 5: Declaration vs Definition
Declaration: inform the compiler of the existence of a variable or function
  void swap(int *a, int *b); // in .h file
Definition: provide function body; allocate memory for local variables
    void swap(int *a, int *b) { // in .c file int temp = *a; *a = *b; *b = temp; }

## Slide 6: Compilation units example
A.h:
int array_len; // global
extern int MAX_SIZE; // global, defined elsewhere
// function declarations
void swap(int *a, int *b);
A.c:
#include "A.h"
// function definition
void swap(int *a, int *b) {
int temp = *a;
*a = *b;
*b = temp;
}
main.c:
#include <stdio.h>
#include "A.h"
int main(void) {
int a = 5;
int b = 15;
swap(a, b);
}
Error?

## Slide 7: Compilers
Bare minimum for a functional compiler
Good compilers
  Produce meaningful errors on incorrect programs
  Produce fast, optimized code
Correct input source program (e.g. C)
Compiler
Functionally equivalent target machine code

## Slide 8
Detailed Compilation Flow
c-file
s-file
assembler
o-file
c-file
s-file
assembler
o-file
c-file
c-file
compiler
o-file
c-file
c-file
compiler
o-file
libraries
compiler
linker
executable

## Slide 9
Detailed Compilation Flow
compiler
o-file
c-file
preproc.
c-file
compiler
o-file
compiler
s-file
compiler
o-file
assembler
o-file
s-file
asembler
o-file
s-file
assembler
o-file
c-file
o-file
c-file
compiler
o-file
libraries
compiler
linker
executable

## Slide 10
Pre-processor
o-file
c-file
c-file
compiler
o-file
compiler
s-file
compiler
o-file
assembler
o-file
s-file
asembler
o-file
s-file
assembler
o-file
c-file
o-file
c-file
compiler
o-file
libraries
compiler
linker
executable
preproc.

## Slide 11: The C pre-processor
Includes – imports header files #include <stdio.h> #include "A.h"
Text substitution, e.g. define constants
  #define NAME value
Macros (inline functions)
  #define MAX(X,Y) (X>Y ? X : Y) // careful with macros!
Conditional compilation
  #ifdef DEBUG
  printf("Debugging message");
  #endif
  $ gcc –DDEBUG ...

## Slide 12: The C pre-processor
Inserts header files to C source code file in response to
  #include <stdio.h> #include "A.h"
Performs macro substitution
  E.g. In response to #define CONST 5
  All references to CONST in source will be replaced by 5
No type checking or anything, just a direct textual replacement
To examine the output gcc pre-processor
  $ gcc –E file.c –o output.c

## Slide 13
Compiler
compiler
o-file
c-file
preproc.
c-file
compiler
o-file
compiler
s-file
compiler
o-file
assembler
o-file
s-file
asembler
o-file
s-file
assembler
o-file
c-file
o-file
c-file
compiler
o-file
libraries
compiler
linker
executable

## Slide 14: Anatomy of a Modern Compiler
Read source program
Break it up into basic elements
Check correctness, report errors
Translate to generic intermediate representation (IR)
Optimize IR
Translate IR to ASM
Optimize ASM
Source
Code
Front-end
(Analysis)
Back-end
(Synthesis)
Target
Code
Intermediate
Representation

## Slide 15: Frontend Stages
int x = 3;
int y = x + 7;
while (x != y) {
if (x > y) {
x = x – y;
} else {
y = y – x;
}
}
Lexical analysis (scanning): Source List of tokens
(“int”, KEYWORD)
(“x”, IDENTIFIER)
(“=”, OPERATOR) (“3”, INT_CONSTANT)
(“;”, SPECIAL_SYMBOL) (“int”, KEYWORD)
(“y”, IDENTIFIER)
(“=”, OPERATOR)
(“x”, IDENTIFIER)
(“+”, OPERATOR) (“7”, INT_CONSTANT)
(“;”, SPECIAL_SYMBOL)
(“while”, KEYWORD) (“(”, SPECIAL_SYMBOL)
...

## Slide 16: Frontend Stages
Lexical analysis (scanning): Source List of tokens
Syntactic analysis (parsing): Tokens Syntax tree
Compound statement
op
=
var x
const 3
op
=
var y
op
+
var x
const 7
while
op
!=
var x
var y
if
op
>
var x
var y
op
=
var x
op
-
var x
var y
op
=
var x
op
-
var x
var y
test
body
test
then
else

## Slide 17: Frontend Stages
int x = "bananas";
Line 1: error, invalid conversion from string constant to int
Syntax OK
Semantically (meaning) WRONG
Consider:
Lexical analysis (scanning): Source List of tokens
Syntactic analysis (parsing): Tokens Syntax tree
Semantic analysis (mainly, type checking)
op
=
var x
const “bananas”
statement list
Var | Type
x | int

## Slide 18: Intermediate Representation (IR)
Internal compiler language that is:
– Language-independent
Machine-independent
Easy to optimize
Why yet another language?
– Assembly does not have enough
info to optimize it well
– Enables modularity and reuse
Analysis (frontend)
Synthesis (backend)
IR
C frontend
IR
opt
IR
C++ frontend
Java frontend
x86 codegen
ARM
codegen
Beta codegen
IR

## Slide 19: Data flow graph (DFG)
Represents flow of data inside “basic block”
Basic blocks
  Code with one entry one exit
  May have a branch at the end, not before
Does not represent control.
Describes the minimal ordering requirements on operations.
Static Single Assignment is employed to ease optimizations

## Slide 20: Static Single Assignment (SSA)
If a variable is assigned more that once in the source code:
  SSA keeps only the first assignment
  The rest of the assignments are renamed to temporary variables
x = a + b;
y = c - d;
z = x * y;
y = b + d;
Original basic block
x = a + b;
y = c - d;
z = x * y;
y1 = b + d;
After SSA

## Slide 21: Data Flow Graph Example
x = a + b;
y = c - d;
z = x * y;
y1 = b + d;
After SSA
+
-
+
*
DFG
a
b
c
d
z
x
y
y1

## Slide 22: DFG and Partial Orders
Partial Orders:
1) a + b, c - d
2) x * y, b + d;
These two pairs of operations can be performed in any order
+
-
+
*
DFG
a
b
c
d
z
x
y
y1

## Slide 23: Control-Data Flow Graph (CDFG)
Represents control and data flow
  Nodes: basic blocks
  Edges: branches between basic blocks

## Slide 24: CDFG Example
if (cond1) bb1();
else bb2();
bb3();
switch (test1) {
case c1: bb4(); break;
case c2: bb5(); break;
case c3: bb6(); break;
}
cond1
bb1()
bb2()
bb3()
bb4()
test1
bb5()
bb6()
T
F
c1
c2
c3

## Slide 25: CDFG Example
int x | = 3; |  | 
int y | = x + | 7; | 
while | (x != | y) | {
if (x > y) { x = x – y;
} else {
y = y – x;
}
}
x = 3
y = x + 7
if (x != y)
if (x > y)
x = x - y
y = y - x
if (x != y)
start
end
T
F
T
F
T F

## Slide 26: IR Optimization
Machine independent optimizations
  Code optimizations independent of the target architecture
  e.g. dead code elimination, constant propagation, constant folding etc.
Machine dependent optimizations
  Specifically aim at target architecture
  May not be applicable directly across different architectures
  e.g. Instruction selection, register allocation etc.

## Slide 27: IR Optimization
Perform a set of passes over the CFG
  Each pass does a specific, simple task over the CFG
  By repeating multiple simple passes on the CFG over and over, compilers achieve very complex optimizations
Example optimizations:
  Dead code elimination: Eliminate assignments to variables that are never used, or basic blocks that are never reached
  Constant propagation: Identify variables that are constant, substitute the constant elsewhere
  Constant folding: Compute and substitute constant expressions

## Slide 28: Example IR Optimizations
int | x | = | 3;
int | y | = | x + 7;
int | z | = | 2*y;
if (x < y) {
z = x/2 + y/3;
} else {
z = x*y + y;
}
x = 3
y = x + 7
z = 2*y
if (x < y)
_t1 = x/2
_t2 = y/3
z = _t1 + _t2
start
end
_t3 = x*y
z = _t3 + y
T
F
NOTE: Expressions with > 2 vars or constants
broken down in multiple assignments,
using temporary variables

## Slide 29: Example IR Optimizations
int | x | = | 3;
int | y | = | x + 7;
int | z | = | 2*y;
if (x < y) {
z = x/2 + y/3;
} else {
z = x*y + y;
}
x = 3
y = x + 7
z = 2*y
if (x < y)
_t1 = x/2
_t2 = y/3
z = _t1 + _t2
start
end
_t3 = x*y
z = _t3 + y
1.
2.
3.
Dead code elim
Constant propagation
Constant folding
y = 3 + 7
y = 10
if (3 < y)
_t1 = 3/2
_t3 = 3*y
T
F
_t1= 1

## Slide 30: Example IR Optimizations
int | x | = | 3;
int | y | = | x + 7;
int | z | = | 2*y;
if (x < y) {
z = x/2 + y/3;
} else {
z = x*y + y;
}
x = 3
y = 10
if (3 < y)
_t1 = 1
_t2 = y/3
z = _t1 + _t2
start
end
_t3 = 3*y
z = _t3 + y
if (3 < 10)
T
F
if (true)
_t2=10/3
_t2 = 3
_t3=3*10
_t3 = 30
z=1+_t2
z=_t3 + 10
1.
2.
3.
4.
5.
6.
Dead code elim
Constant propagation
Constant folding
Dead code elim
Constant propagation
Constant folding

## Slide 31: Example IR Optimizations
int | x | = | 3;
int | y | = | x + 7;
int | z | = | 2*y;
if (x < y) {
z = x/2 + y/3;
} else {
z = x*y + y;
}
y = 10
if (true)
_t1 = 1
_t2 = 3
z = _t1 + _t2
start
end
_t3 = 30
z = _t3 + 10
T
F
1.
2.
3.
4.
5.
6.
7.
Dead code elim
Constant propagation
Constant folding
Dead code elim
Constant propagation
Constant folding
Dead code elim

## Slide 32: Example IR Optimizations
int | x | = | 3;
int | y | = | x + 7;
int | z | = | 2*y;
if (x < y) {
z = x/2 + y/3;
} else {
z = x*y + y;
}
_t1 = 1
_t2 = 3
z = _t1 + _t2
start
end
z = 1+3
z = 4
1.
2.
3.
4.
5.
6.
7.
8.
9.
Dead code elim
Constant propagation
Constant folding
Dead code elim
Constant propagation
Constant folding
Dead code elim
Constant propagation
Constant folding
10.Dead code elim

## Slide 33: Example IR Optimizations
Dumb repetition of simple transformations on CFGs
Extremely powerful optimizations
More optimizations by adding passes: Common
subexpression elimination, loop-invariant code motion, loop unrolling…
Dead code elim
Constant propagation
Constant folding
Dead code elim
Constant propagation
Constant folding
Dead code elim
Constant propagation
Constant folding
10. Dead code elim
11. Constant propagation
12. Constant folding
13. Dead code elim
14. Constant propagation
15. Constant folding
No changes in 13,14,15
⇒ DONE
z = 4
start
end
int | x | = | 3;
int | y | = | x + 7;
int | z | = | 2*y;
if (x < y) {
z = x/2 + y/3;
} else {
z = x*y + y;
}
1.
2.
3.
4.
5.
6.
7.
8.
9.

## Slide 34: Code Generation
Translate optimized IR to assembly
Register allocation: Map variable to registers
  If #variables > #registers, map some to memory and load/store when needed
Translate each assignment to instruction
  Some assignments may require more than one instruction if ISA does not have operations
Emit each basic block: labels, assignments and branches
Lay out basic blocks, remove superfluous branches
ISA and CPU specific optimization
  E.g. reorder instructions if possible

## Slide 35: Putting It All Together
Source code
int x = 3;
int y = x + 7; while (x != y) {
if (x > y) {
x = x – y;
} else {
y = y – x;
}
}
x = 3
y = x + 7
if (x != y)
if (x > y)
x = x - y
y = y - x
if (x != y)
start
end
T
F
T
F
T F
x = 3
y = 10
if (x > y)
x = x - y
y = y - x
if (x != y)
start
end
T F
T F
IR
Optimized IR

## Slide 36: Putting It All Together
x = 3
y = 10
if (x > y)
x = x - y
y = y - x
if (x != y)
start
end
T F
T F
0
1
2
3
4
BBL0:
MOVE(3, R0) MOVE(10, R1) BR(BBL1)
BBL1:
CMPLT(R1, R0, R2) BT(R2, BBL2) BR(BBL3)
BBL2:
SUB(R0, R1, R0) BR(BBL4)
BBL3:
SUB(R1, R0, R1) BR(BBL4)
BBL4:
CMPEQ(R1, R0, R2) BT(R2, end) BR(BBL1)
end:
Allocate registers:
x: R0, y: R1
Produce each basic block:
3. Lay out BBs, removing superfluous branches:
BBL0:
BBL1:
BBL3:
BBL2: BBL4:
MOVE(3, R0)
MOVE(10, R1)
CMPLT(R1, R0, R2)
BT(R2, BBL2)
SUB(R1, R0, R1)
BR(BBL4)
SUB(R0, R1, R0) CMPEQ(R1, R0, R2) BF(R2, BBL1)
end:

## Slide 37: Summary: Modern Compilers
Source code
Lexical analysis
Syntactic analysis
Semantic analysis
Generate IR
Optimize IR
Generate ASM
Tokens
Syntax tree
Type-checked syntax tree
IR
IR (optimized)
High-quality assembly
(often > hand-coded!)
Frontend (analysis)
Produces IR if correct program
Produces meaningful errors
Backend (synthesis)
Produces optimized
program

## Slide 38: Compiler Optimizations

## Slide 39: Loop Transformations
Why is it important
  Programs spends lots of time in loops
Goal
  Reduce loop overhead
  Increase opportunities for other optimizations
  Improve pipeline and memory system performance

## Slide 40: #1: Loop Unrolling
Duplicates loop body ‘n’ times and adjust loop bounds
  Reduces number of comparisons/branches to test loop exit
    Branches are big performance bottleneck in hardware
  Increases loop body size
    Enables more optimizations
    More register pressure
for (i=0; i<4; i++)
a[i] = b[i] * c[i];
for (i=0; i<4; i+=2) {
a[i] = b[i] * c[i];
a[i+1] = b[i+1] * c[i+1];
}

## Slide 41: #2: Loop Fusion
Combines two (or more) loops into one
  May improve data locality
  Reduces loop overhead
  May enable better instruction scheduling
for (i=0; i<N; i++)
a[i] = b[i] * c[i];
for (i=0; i<N; i++)
w[i] = a[i] * d[i];
for (i=0; i<N; i++) {
a[i] = b[i] * c[i]; w[i] = a[i] * d[i];
}
May hurt data locality
May hurt I-cache hit rate

## Slide 42: #3: Loop Distribution/Fission
Divides a loop into two (or more) loops
Enables optimizations: 2nd loop is parallel loop
Reduces register pressure
Increases loop overhead
for (i=1; i<N; i++)
a[i] = a[i-1] * 5;
for (i=1; i<N; i++)
c[i] = b[i] * 10;
for (i=1; i<N; i++) {
a[i] = a[i-1] * 5;
c[i] = b[i] * 10;
}

## Slide 43: #4: Loop Interchange
Switches the order of loops in a loop nest
Improves data locality and parallelism
for (i=0; i<N; i++)
for (j=0; j<M; j++)
c[j][i] = a[j][i] * 5;
for (j=0; j<M; j++)
for (i=0; i<N; i++) c[j][i] = a[j][i] * 5;

## Slide 44: #5: Loop Tiling
Breaks a loop into a set of nested loops
  Each inner loop operates on a subset of data
Changes memory access pattern: Can improve locality
for (i=0; i<N; i++)
for (j=0; j<M; j++)
f(i, j);
for (i=0; i<N; i+=2)
for (j=0; j<M; j+=2)
for(ii=i; ii<min(i+2, N); ii++)
for(jj=j; jj<min(j+2, N); jj++)
f(ii, jj);
(0,0) (0,1) (0,N-1)
(1,0) (1,1) (1,N-1)
(0,0) (0,1)
(1,0) (1,1)
(0,0) (0,1)
(1,0) (1,1)
...

## Slide 45
Replaces call with the body of the callee (called function)
Programmer can ask compiler to inline a function
  C provides inline keyword
Compiler itself can inline a function if deemed beneficial
Procedure/Function Inlining
int foo (int a, int b, int c) {
return a + b - c;
}
z = foo(w, x, y);
z = w + x - y;

## Slide 46
Function calls can be costly
  Direct costs: arguments and results passing, call/return (branch) instructions, stack frame maintenance etc
  Indirect costs: breaks intra-procedural analysis to inter-procedural analysis (which is more complex)
Inlining removes these costs
Downside
  Can increases code size
  Can reduce instruction cache hit rate
Why Procedure/Function Inlining

## Slide 47
Registers temporarily hold variables
Aim: Allocate registers to variables such that memory accesses are minimized
  Good register allocation is key to performance as memory accesses can be costly (imagine cache misses)
Compilers analyze lifetime of variables for register allocation
Programmers could hint which variables to keep in registers
  C supports register keyword
  Modern compilers just ignore it!
Some variables always need to be in memory
  volatile keyword provides this functionality
  Still brought to a register for using the value
Register Allocation

## Slide 48
Register Lifetime Analysis
w = a + b; t = 1
x = c + w; t = 2
y = c + d; t = 3
time
a b
c d w x y
1
2
3

## Slide 49
Register Allocation Example
a b
c
d
w
x
y
1 2
3 time
a
b
w
x
c
d
y
Graph Coloring
Edges between variable that are live at the same time
Represent each register with a color
Color the nodes with as few colors as possible
  No edge must share a color
NP-complete
  Compilers use heuristics to reach a good solution
3 registers a r0
b r1
w r2
x r1
c r0
y r2
d r1

## Slide 50
Instruction scheduling changes the lifetime of variables
  Changes number of registers required
Register Allocation (Impact of Instruction Scheduling)
w = a + b;
x = c + d;
y = x + e;
z = w - b;
5 registers required
w = a + b;
z = w – b;
x = c + d;
y = x + e;
Only 3 registers required

## Slide 51
IR code can be translated to a number instruction sequences depending types of instructions in ISA
IR expressions are represented as graphs (CDFG)
  Find the best template for expression
  The template should minimize the chosen cost metric
Instruction Selection
Templates
*
MUL
+
ADD
*
+
MADD
+
Expression
*

## Slide 52
Assembler
compiler
o-file
c-file
preproc.
c-file
compiler
o-file
compiler
s-file
compiler
o-file
assembler
o-file
s-file
asembler
o-file
s-file
assembler
o-file
c-file
o-file
c-file
compiler
o-file
libraries
compiler
linker
executable

## Slide 53
Generate machine instructions (binary) from assembly instructions (symbolic)
  One to one translation
Translate labels into addresses
Handle pseudo-ops
Two pass approach
  First pass: Generate symbol table
  Second pass: resolve labels and generate machine instructions
Assembler

## Slide 54
Symbol Table
High Level Language Code
Assembly Code
int a = 1;
int b = 2;
while(a != b) {
// loop body
}
ldr r0, =vars
ldr r1, [r0]
ldr r2, [r0, #4]
loop: cmp r1, r2
beq end
; loop body
b loop
end:
Generating symbol table:
  Scan the file to collect labels and their addresses
    Addresses are generally relative to the first instructions in the file

## Slide 55
Symbol Table
High Level Language Code
Assembly Code
int a = 1;
int b = 2;
while(a != b) {
// loop body
}
ldr r0, =vars
ldr r1, [r0]
ldr r2, [r0, #4]
loop: cmp r1, r2
beq end
; loop body
b loop
end:
loop Start+12
end Start+28
Symbol Table

## Slide 56
Symbol Table
Assembly Code
ldr r0, =vars
ldr r1, [r0]
ldr r2, [r0, #4]
loop: cmp r1, r2
beq start+28
; loop body
b start+12
end:
loop Start+12
end Start+28
Symbol Table
Substitute the labels with addresses.
ldr r0, =vars
ldr r1, [r0]
ldr r2, [r0, #4]
loop: cmp r1, r2
beq end
; loop body
b loop
end:

## Slide 57
Symbol Table
What if label is defined in a different file
Assembler can’t resolve such labels
  It’s the job of the linker
external reference
entry point
label1 ADD R1, R2, R3
B label2
label2
ADD R4, R1, R2
ADD R3, R4, R5
file 1
file 2

## Slide 58
Output of assembler
Several standards
  ELF (Unix), ECOFF (Windows), Mach-O (OS X)
Object file includes
  Symbol table
  Program code (.text segment)
  Data (.data segment)
  Information about relocatable parts
  Debug data (references to source files)
Object File

## Slide 59
Linker
compiler
o-file
c-file
preproc.
c-file
compiler
o-file
compiler
s-file
compiler
o-file
assembler
o-file
s-file
asembler
o-file
s-file
assembler
o-file
c-file
o-file
c-file
compiler
o-file
libraries
compiler
linker
executable

## Slide 60
Takes multiple object files and libraries and generates one executable file
  Combines all object file segments (text, data)
  Determines start address for all modules
  Combines all symbol tables
  Resolves all symbols
    Transforms relative address to absolute addresses
    Produces an error if cannot find a label/symbol in merged symbol table
Linker

## Slide 61
Most operating systems can link modules at load time
  e.g. shared libraries (.so on linux platforms)
  Saves storage space
Dynamic Linking

## Slide 62
Next courses
Next lecture
  Introduction to Operating Systems
What’s next?
TDT4205: Compiler Construction